NDLCOM and its setup in XILINX

File setup
- Files are available in fpgasvn/dev/design/NDLCom/trunk/basic
- create a new project in xilinx , with the name NDLCom echo
- Add all the files from “Add source”
- Search for the files which are missing and add them
- Ad libraires like zynq, encode, decode, spartan6 ( used only with spartan 6 fpga, but still added) , ONLY by creating new libraries
- libraries can be created in libraries tab >> right click >> NEW VHDL Library, and then give the correct name and add the files from the directory.
- Deviceclasses and Device packages SHOULD BE added from common gui. Path is istruct>>lib>>Robotconfig>>vhdl. Add both the files.
Explanation

NDLCom Basic Consists of instantiates five designs

rtc_mod : Real time clock module for an internal time in us.

NDLCom wrapper : NDLCom wrapper which handles the communication via NDLCom

simple_spiprom_interface : This module allows page read/write and sector erase at an SPI EEPROM in 1bit mode

register_access : This module provides the register access functionality that comes with the NDLCom framework (read/write register). It also provides a prom-connection to read/write prom registers from/to it.

InSystemProgramming module :